## Slide 1: Development Flow for Edge AI Devices
ML MODEL DEVELOPMENT (MLOps)
CLASSIC EMBEDDED DEVELOPMENT
Model searcher
Model Compressor
Trained
ML Model
Weight clustering
Quantization
Compile
Validate
Optimized ML Model
Arm tools integrate here
Data
Use-Case
Sensor
Audio
Video
Input Interface
Signal Conditioning
Optimized ML Model
Output Interface
SDS Data Capturing
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 2: Development Flow for Edge AI Devices
DATA STREAM
ML Input Data
Sensor
Audio
Video
Input Interface
Signal Conditioning
Optimized ML Model
Output Interface
SDS Stream Interface
ML Output Data
SDS Stream Interface
Physical Sensor Input Data
SDS Stream Interface
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 3: SDS-Framework: Record Real-world Data and Playback to AVH
SDSIO-Server
Input Interface
Sensor Input
SDS Stream
SDSIO-Server
Algorithm under Development
Algorithm under Development
Record physical sensor (real-world) data using MCU hardware
Playback real-world data in CI
SDS Data Files have multiple use cases:
Input for ML Algorithm development
Input for Filter Designers (i.e. ASN)
When capturing Algorithm outputs, validation for regression
SDS Interfaces can be based on
https://github.com/ARM-software/CMSIS-DSP/tree/main/ComputeGraph
Currently under development
https://github.com/ARM-software/SDS-Framework
Simplify Development of Embedded Applications that utilize DSP or ML algorithms with Sensor/Audio Input
Physical Sensor
Physical Sensor Data
Physical Sensor Data
MICROCONTROLLER HARDWARE
SIMULATION
SDS Stream

## Slide 4: Development Flow for Edge AI Devices
DATA STREAM UNDER DEVELOPMENT
ML Input Data
Signal Conditioning
Optimized ML Model
SDS Stream
in write mode
ML Output Data
Physical Sensor Input Data
SDS Stream
in read mode
SDSIO-Server running on development host system
SDSIO INTERFACE
or
SDS Stream
in write mode
Output
DATA STREAM UNDER DEVELOPMENT
Sensor
Audio
Video
Input Interface
Signal Conditioning
Optimized ML Model
Output
ML Input Data
SDS Stream
in write mode
ML Output Data
Physical Sensor Input Data
SDS Stream
in write mode
SDSIO INTERFACE
or
SDS Stream
in write mode
SDSIO-Server running on development host system
or
RTT
or
RTT
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 5: Challenge: Validate and Optimize Algorithms with Real World Data
github.com/ARM-software/SDS-Framework
DATA STREAM UNDER DEVELOPMENT
ML Input Data
Signal Conditioning
Optimized ML Model
SDS Stream
in write mode
ML Output Data
Physical Sensor Input Data
SDS Stream
in read mode
SDSIO-Server running on development host or AVH simulation
SDSIO INTERFACE
SDS Stream
in write mode
Output
DATA STREAM UNDER DEVELOPMENT
Sensor
Audio
Video
Input Interface
Signal Conditioning
Optimized ML Model
Output
ML Input Data
SDS Stream
in write mode
ML Output Data
Physical Sensor Input Data
SDS Stream
in write mode
SDSIO INTERFACE
SDS Stream
in write mode
SDSIO-Server running on development host or file system on target
Capture real-world data streams in hardware
Use same data streams to repeat tests
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 6
DATA STREAM UNDER DEVELOPMENT
Signal Conditioning
Optimized ML Model
SDS Stream
in write mode
SDS Stream
in read mode
SDSIO INTERFACE
SDS Stream
in write mode
Output
DATA STREAM UNDER DEVELOPMENT
Sensor
Audio
Video
Input Interface
Signal Conditioning
Optimized ML Model
Output
SDS Stream
in write mode
SDS Stream
in write mode
SDSIO INTERFACE
SDS Stream
in write mode
FILE ACCESS
FILE ACCESS
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
SCinput.0.sds
SCoutput.0.sds
MLoutput.0.sds
Playback:
SCinput.*.sds files are the input (as per sdsio.yml)
New SCoutput.*.sds and Mloutput.*.p.sds files are generated
RTT
RTT
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 7: SDS software developer framework DSP / ML algorithm design
DATA STREAM UNDER DEVELOPMENT
Signal Conditioning
Optimized ML Model
Output
SDSIO INTERFACE
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
SCinput
SCoutput
MLoutput
SDS
Stream
SDS
Stream
Sensor
Audio
Video
Input Interface
SDS
Stream
Recording
SDS Stream
Playback
Any mode
Active during
Metadata files describe data stream content
DSP / ML algorithms operate on time-series data streams, such as sensor data, audio samples, or video frames, using fixed or variable-size blocks.
SDS is a software developer framework for DSP / ML:
Handle sensor, audio, and video streams flexibly.
Multiple streams with time-drift handling for sensor fusion.
Record real-world target data for analysis and development.
Replay streams on hardware or simulation for validation.
Captured data streams simplify development:
Validate input streams and algorithm outputs.
Provide input for DSP filter design or ML model training.
Enable reproducible regression tests.
Use artificially generated input data for algorithm testing.
SDS v3 adds a control interface in the SDSIO-Server:
Operate through SDS VS Code extension on in CLI mode.
Record and playback mode in the same firmware image.
Use flags to configure algorithms or run A/B tests.
Manage playback streams for regression testing.
Deploy to hardware:  SDS Template Application
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 8: SDS software developer framework DSP / ML algorithm design
DATA STREAM UNDER DEVELOPMENT
Signal Conditioning
Optimized ML Model
Output
SDSIO INTERFACE
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
SCinput
SCoutput
MLoutput
SDS
Stream
SDS
Stream
Sensor
Audio
Video
Input Interface
SDS
Stream
Recording
SDS Stream
Playback
Any mode
Active during
Metadata files describe data stream content
DSP / ML algorithms operate on time-series data streams, such as sensor data, audio samples, or video frames, using fixed or variable-size blocks.
SDS is a software developer framework for DSP / ML:
Handle sensor, audio, and video streams flexibly.
Multiple streams with time-drift handling for sensor fusion.
Record real-world target data for analysis and development.
Replay streams on hardware or simulation for validation.
Captured data streams simplify development:
Validate input streams and algorithm outputs.
Provide input for DSP filter design or ML model training.
Enable reproducible regression tests.
Use artificially generated input data for algorithm testing.
SDS v3 adds a control interface in the SDSIO-Server:
Operate through SDS VS Code extension on in CLI mode.
Record and playback mode in the same firmware image.
Use flags to configure algorithms or run A/B tests.
Manage playback streams for regression testing.
Deploy to hardware:  SDS Template Application
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 9: Data Labelling and Regression Test Configuration
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
SCinput.0.sds
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
SCinput.0+case1.sds
SCinput.0+case2.sds
Split SDS files
timeslot
block size
data block
timeslot
block size
data block
timeslot
block size
SDS file format
sample #0
sample #1
:
sample #n
granularity: tick-frequency
block-frequency
Binary input or output of a compute node
sample-frequency
X         
Y         
Z         
t
data block #1
data block #2
MEMS capturing with 3,5kHz ±5% sample frequency
audio signal capturing with 8kHz sample frequency

## Slide 10: SDS: flexible stream management for sensor and audio data
Supports the whole development cycle: data recording, analysis, ML training, playback
X         
Y         
Z         
t
SDS Metadata File ‘SensorX.sds.yml’
SDS Data Files ‘SensorX.<idx0>.sds’ ‘SensorX.<idx1>.sds’
data block #1
data block #2
MEMS capturing with 3,5kHz ±5%
audio signal capturing with 8kHz
Single or multiple data streams, including sensor fusion with clock deviations
  Sensors may have independent clock sources with tolerances
SDS Metadata file describes content of SDS data files
Python-based utilities for recording, playback, visualization, data conversion, and algorithm verification with off-line tools

## Slide 11
sds_buffer.c/h Circular Buffer Handling
A circular buffer management for each data stream triggers events back to the SDS Stream Interface when a buffer threshold is reached.
sdsio_x.c/sdsio.h SDSIO Client Interface
*.sds data files
This SDSIO Client Interface implements the access to *.sds data files. Multiple SDSIO Client implementations are available that interface to file system, network, UART, USB, or RTT.
The SDS Stream Interface implements non-blocking, thread-safe functions to read or write data streams.
sds.c/h SDS Stream Interface
Data stream application under development

## Slide 12: SDS Recorder https://github.com/Arm-Examples/sds-examples
SDS.csolution.yml Data streaming test framework for DSP and ML algorithms
Record/Playback SDS Data Files via Network, RTT, USB, File System
Layer Type: SDSIO
Board Hardware Interface Provided in BSP
Layer Type: Board
Check SDSIO interface with user configurable bandwidth parameters
DataTest.cproject.yml
Verify and optimize user algorithms with repeatable data
AlgorithmTest.cproject.yml
target-types select between hardware
and simulation
Add user algorithm and data stream input interface
Start/stop, recording, and playback selected at runtime using sdsFlags

## Slide 13: Challenge: Validate and Optimize Algorithms with Real World Data
github.com/ARM-software/SDS-Framework
SDS Stream
in read mode
ALGORITHM UNDER DEVELOPMENT
Input Interface
Algorithm
Output
Algorithm Output Data
Physical Input Data
SDS Stream
in write mode
SDSIO INTERFACE
SDS Stream
in write mode
SDSIO-Server running on development host or file system on target
Capture real-world data streams in hardware
Use same data streams to repeat tests
ALGORITHM UNDER DEVELOPMENT
Algorithm
Output
Algorithm Output Data
Physical Input Data
SDSIO INTERFACE
SDS Stream
in write mode
SDSIO-Server running on development host or AVH simulation
RTT
RTT
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 14: Current Status of CMSIS-DSP Compute Graph
Documentation and several usage examples available today
Usage Steps with current tool flow:
  Describe the graph using Python
    Consider: No. of I/O of each node, data types, number of I/O samples produced/consumed
  Compute the optimized static scheduling from the graph (using Python)
  Generate the C++ scheduler
  Create C++ wrapper for the algorithm nodes (if they are not already available)
Signal conditioning
Filters
Echo, noise canceller
White balance
Feature extraction
Spectral data
MFCC (audio)
Convolution (pixel)
Classifier
Classical ML Deep learning (NN)
In
Out
The smarter the features, the lower the complexity of the classifier.
  More “DSP” pre-processing helps lowering the system complexity
We propose to form a working group with eco-system partners
 Video Recording of partner meeting

## Slide 15: Record real-world data with Synchronous Data Streaming (SDS)
Simplify Development of Embedded Applications that utilize DSP or ML algorithms with Sensor/Audio Input
MCU Device
Software on Physical Board
Microcontroller Hardware
SDS Stream
Interface
SDS Stream connects via different channels
Algorithm under Development
Capture physical sensor (real-world) data using the original Microcontroller target hardware
SDS Data Files
*.gyroscope.sds
Audio Interface
Microphone Input
SDS Data Files
*.microphone.sds
z
y
x
Training Data
Validation Data
Test Data
Data conversion to ML training platform can be automated.
The SDS framework provides methods to record real-world data for analysis and development.
Input to Digital Signal Processing (DSP) development tools such as filter designers
Input to Machine Learning (ML) model classification, training, and performance optimization.
SDS framework is an open-source project: github.com/Arm-Software/SDS-Framework
MEMS Sensor Interface
Gyroscope Sensor

## Slide 16: SDS enables playback of real-world data for algorithm testing
AVH VSI
Software on Arm Virtual Hardware
Software on Physical Board
MCU Device
Combined with AVH it enables repeatable test automation in CI systems and MLOps cloud services
MEMS Sensor Interface
Gyroscope Sensor
Microcontroller Hardware
SDS Stream
Interface
SDS Stream connects via different channels
Algorithm under Development
SDS Data Files
gyroscope.*.sds
Audio Interface
Microphone Input
SDS Data Files
microphone.*.sds
z
y
x
VSI Sensor Interface
Virtual Streaming Interface #1
Arm Virtual Hardware (AVH-FVP)
Algorithm under Development
VSI Audio Interface
Virtual Streaming Interface #2
SDS Data Files
gyroscope.*.sds
SDS Data Files
microphone.*.sds
Same algorithm is verified on precise processor simulation model

## Slide 17: SDS Data Buffer and Stream Interface
Data I/O via blocking devices (fread, fwrite)
Data Recording via File I/O, Serial, Socket
Circular Data Buffers
sds_buffer.h Circular Buffer Handling
sdsio.h Blocking R/W Interface (i.e. file I/O)
sds.h Data Stream Interface
in write mode
sds.h Data Stream Interface in read mode
*.sds Data Files ‘sensorX.0.sds’ ‘sensorX.1.sds’
Meta Info User supplied ‘sensorX.sds.yml’
Data Playback via File I/O, Serial, Socket, or AVH VSI

## Slide 18
*.sds Data Files ‘sensorX.0.sds’ ‘sensorX.1.sds’
Metadata User supplied ‘sensorX.sds.yml’

## Slide 19: Development Flow for Edge AI Devices
ML_In SDS Files
Video
Input Interface
Signal Conditioning
Optimized ML Model
Output Interface
SDS Stream in read/write mode
ML_Out SDS Files
SDS Stream
in write mode
Video_In SDS Files
SDS Stream (optional) in write mode
ML_In SDS Files
Optimized ML Model
Output Interface
SDS Stream
in read mode
ML_Out SDS Files
SDS Stream
in write mode
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 20
SDS.csolution.yml Data streaming test framework for DSP and ML algorithms
Record/Playback
SDS data files via
SDSIO-Server USB
Layer Type: SDSIO
Board Hardware Interface Copied from Alif DFP/BSP Adopted for Video input/output
Layer Type: Board
Trained PyTorch Model with ExecuTorch run-time optimized for Ethos-U85
Layer Type: AI / ExecuTorch
Configured example for Alif AppKit-E8-AIML Video input/output
AlgorithmTest.cproject.yml
target-types select between hardware
and simulation
Start/stop, recording, and playback selected at runtime using sdsFlags

## Slide 21
USB SoC
USB Debug UART
JTAG Debug
Camera
Connect to CMSIS-DAP Unit and pyOCD
SDSIO-Server USB
Alif AppKit-E8-AIML
J-Link Server Serial Monitor

## Slide 22: SDSIO-Server Firmware / Monitor Interface
Firmware
Monitor program
SDSIO-Server
or
or
Firmware Protocol
Monitor Protocol

## Slide 23
Target hardware with SDS firmware configured for USB interface
USB
Host Computer
SDSIO-Server USB Mode
SDS VS-Code extension or
MLOps system
Monitor Interface
Target hardware with SDS firmware configured for Network interface
Host Computer
SDSIO-Server Socket Mode (listen)
SDS VS-Code extension or
MLOps system
Monitor Interface
Ethernet
LAN
Target hardware with SDS firmware configured for RTT interface
Host Computer
SDSIO-Server Socket Mode (connect)
SDS VS-Code extension or
MLOps system
Monitor Interface
Debug